## Slide 1: Casey Lake, North St. Paul
CE 5511 Urban Hydrology and Land Development
Instructor: John S. Gulliver
Presented by:
Joshua Balzer Stephanie Hatten
Maria Garcia-Serrana Delaney Kolb

## Slide 2: Introduction
Casey Lake subwatershed
Goal: Provide stormwater treatment to reduce pollutant loading
  Total suspended solids (TSS) and total phosphorous (TP)
4 solutions were analyzed
Bioretention cell from Ramsey Conservation District Report

## Slide 3: Background
Casey Lake is considered a wetland rather than a lake
  Classified as Management Class B
  High quality wetland that requires a minimum of 25’ buffer from development
  TP based on water quality for shallow lakes
    <60 ug/L
  Current TSS and TP is unknown as there is no water quality data available

## Slide 4: Methods
Porous Asphalt
Two locations:
  Trail along the lake
  Parking Lot
Soils HSG A and B:
  Water infiltrates
Maintenance is key:
  Sweeping 3 times per year
PERMEABLE PAVEMENTS

## Slide 5: Methods
PERMEABLE PAVEMENTS
Trail:
  Base-Iron Enhanced Sand (88% TP)
    Drainage area: 8.7ac
    Area of PP: 800 m2
    Cost of installation: $196,980
P8 Model:
Infiltration Trench
CN=40 (WERF)
Parking Lot:
  Base- Aggregates
    Drainage area: 0.75ac
    Area of PP: 2,954 m2
    Cost of installation: $$128,652

## Slide 6: Methods
Route existing storm sewer into infiltration basin
Size for a 1.1 inch water quality storm
69-acre drainage area
  CN = 75
  38% impervious
INFILTRATION BASIN

## Slide 7: Methods
Sandy Loam Soil Assumption
Size of basin: 1.32 acres
Modeled in P8
Cost of Installation: $238, 326
INFILTRATION BASIN

## Slide 8: Methods
Leaves and street debris are a major source of phosphorus and suspended solids
Street sweeping removes pollutants before they reach stormwater systems
STREET SWEEPING

## Slide 9: Methods
STREET SWEEPING
Street sweeping removes significant amounts of pollutants according to current research
Increased sweeping frequency is a cost effective method
Credit: http://www.tymco.com//

## Slide 10: Methods
Retrofit with SAFL Baffles
SAFL Baffle is a post-construction stormwater pretreatment system that can be installed in existing sump structures
Helps increase settling of sediments flowing through the system
Vacuum truck is used to remove sediments
SUMP CLEANING

## Slide 11: Methods
Modeled with Barr Engineering SHSAM program
  Sizing Hydrodynamic Separators and Manholes
Cleaned once a year
SUMP CLEANING

## Slide 12: Results

## Slide 13: Conclusions
Street Sweeping
  Highly efficient pollutant remover when optimized
  Very easy to implement
Sump Cleaning/SAFL Baffle installation
  Low-cost measure
  Good results for Phosphorous removal

## Slide 14
Thanks for your attention
We look forward to your questions and participation