## Slide 1
Bluff to Beach: Sand sources, sinks, and pathways in far western Lake Superior – implications for the genesis and evolution of Minnesota Point
John B. Swenson
Department of Earth and Environmental Sciences
University of Minnesota Duluth
218-726-6844
jswenso2@d.umn.edu
Lake Superior bluff, Douglas County, WI

## Slide 2
Expenditure of tens of millions of taxpayer dollars for mitigation of coastal erosion necessitates sound understanding of sediment pathways and rates
Present a source-to-sink framework for erosion, transport, and deposition of sand in the Duluth coastal region
Provide scientific insight—on geologic timescales—to guide long-term (human timescale) strategic planning
Goals:
Acknowledgments:
Nigel Wattrus (UMD / LLO faculty)
Todd Kremmin (UMD grad student)
Andrew Dennison (UMD grad student)
Crystal Lambert (UMD undergraduate)
Andrew Breckenridge (UWS faculty)
Coastal Erosion Hazard Mapping (CEHM) Task Force colleagues

## Slide 3
Comparing apples to apples: What is Minnesota Point?
Sand bar?
Spit?
Baymouth bar?
Does it matter?
Barrier island separating estuary (drowned river) from open ‘sea’
Key point: Barrier island formation linked to sea-level RISE (simple reason = must drown river to form estuary)

## Slide 4
Long-term lake level change in Duluth area
Change in outlet of Lake Superior @ ~ 1200 yr BP triggers rise in lake level
Lake-level curve from Breckenridge et al. (2016), based in part on earlier work by Johnston et al. (2012), Yu et al. (2013), and Mainville and Craymer (2005)
~ 1200 yr BP (+/- geologic slop)
Birth of Minnesota Point
Rise rate ~ 2.5 – 3.0 mm/a in Duluth = FAST (geologically speaking)
Slowly falling lake level from about 4500 yr BP – 1200 yr BP
‘slow’ fall
Birth of Connor’s & Rice’s Points

## Slide 5
Sand sources: Riverine (fluvial) input
N. Shore: Small catchments, low sediment yield
S. Shore: Small & medium catchments, modest sediment yield
St. Louis: Large catchment, very low sediment yield
Nemadji: Medium catchment, high sediment yield
For all sediment sources:
Mud : Sand ratio ~ 10 : 1
Riverine input trends (big picture):
No significant change in sediment yield for last 4500 years
  Except last 150 years ↔ land-use changes
From 1200 years BP – present, St. Louis & Nemadji progressively disconnected from coastal waters
Sand input (rivers)
From where else might we source sand?

## Slide 6
Sand sources: Bluff erosion
N. Shore: Bedrock cored; veneer of till (‘butter’)
S. Shore: Thick till (~ all ‘butter’)
For all sediment sources:
Mud : Sand ratio ~ 10 : 1
Trends in bluff erosion (big picture):
Minor bluff erosion from 4500 - 1200 years BP
Profound INCREASE in bluff erosion @ 1200 years BP
1200 years BP – present: Bluff erosion driven by long-term lake-level rise
Sand input (bluff erosion)
4500 – 1200 yrs BP
1200 yrs BP – present

## Slide 7
Diabase dike (intrusive rock): More resistant to weathering
Contact between glacial till and underlying volcanic flow (bedrock)
Thin veneer of active beach cobbles
Rapid lake-level rise drives bluff erosion
(Lambert and Swenson, 2016)
Key Point: Nearshore lake-floor geometry holds information about long-term bluff-retreat rates

## Slide 8
Long-term (multi-century) bluff erosion rates
Lambert and Swenson (2016)
Offshore slope
Bedrock-cored north-shore bluff retreat rate ~ 5 cm/yr
Large variability because of mixed lithology, e.g. rhyolite vs. basalt vs. diabase
South-shore bluff retreat rate ~ 50 cm/yr
Mechanically weak, unconsolidated till
Less variability -> homogenous till

## Slide 9
Bluff retreat is driven by rise in lake level from ~1200 yr BP - present
North shore retreat rate ~ cms / year
Large variability (tied to lithology)
South shore retreat rate ~ TENS of cms / year
Less variability (~homogeneous material)
~ 5 cm/yr
~ 50+ cm/yr

## Slide 10
Alberta Clipper
Colorado Low / Texas Hook
Nearly all extratropical cyclone tracks generate period of E – NE flow in the western arm of Lake Superior
Transport pathways: Sand transported during ‘storms’ (cyclones)

## Slide 11
Transport pathways: Net longshore transport of sand near Duluth
E- NE wind
wave crests
wave crests
Longshore sand transport
convergence = deposition (SINK)
Net erosional coastline
Net erosional coastline
Net depositional
coastline
St. Louis & Nemadji Rivers (potentially) add to net sediment convergence

## Slide 12
NET longshore transport
concrete dock: ‘dams’ river of sand
wave crests
Glensheen Mansion
Net longshore transport near Duluth
Transport pathways converge in the Duluth Harbor area. What type of depositional landform results?

## Slide 13
Sand sink: Depositional landform flavor depends on lake-level trend
-
+
lake level
N
N
Bay of Campeche
Grand Traverse Bay, east coast Keweenaw Peninsula
Stable or slowly falling lake level = strandplains
Strandplain = collection of beach ridges reflecting lakeward growth
oldest ridge
younger ridge
modern
all ridges ~ same elevation
Ridges are a bit like tree rings—but not annual

## Slide 14
Depositional landform flavor depends on lake-level trend
N
Albermarle Sound
Rapidly rising lake level = estuaries and barrier islands
Outer Banks
barrier island
estuary (drowned river)
-
+
lake level

## Slide 15
Genesis of Duluth Harbor and Minnesota Point

## Slide 16
(Genetic model) 4500 – 1200 years BP: Slow lake-level fall
Construction of strandplain (now drowned)
No harbor
No estuary
Sand supply mostly from St. Louis and Nemadji Rivers (connected to lake)
Some longshore transport of sand from north- and south-shore rivers
Minor bluff erosion
slow fall
Sand budget ~ 50,000 – 70,000 m3/yr

## Slide 17
Supporting evidence for strandplain beneath harbor
Digitization of 1863 Hearding map by Andy Breckenridge and students
Note curvilinear (arcuate) features in mapped 1863 bathymetry = beach ridges (drowned)
Wiki image of Bathhurst Inlet, Nunavut
An (elusive) feature like this underlies the muddy bottom of the Duluth / Superior harbor
slow fall

## Slide 18
Abandonment (?) and drowning of strandplain
Northwestward growth of Minnesota Point (?)
Harbor and estuary formation
Today: Dominant sand source
(Genetic model) 1200 years BP - present: Rapid lake-level RISE
rapid rise
Erosion of south-shore bluffs dominates sand budget
Order of magnitude less from north shore bluffs
St. Louis and Nemadji Rivers contribute relatively little due to progressive drowning and trapping in estuary

## Slide 19
~ 90 m growth in 80 years
Overlay of 2017 (color) satellite image and 1938 aerial photo.
The ‘infrastructure’ problem: Starvation
~ 90 m erosion in 80 years
Superior entry forms nearly perfect ‘dam’ in the ‘river of sand’ from south shore

## Slide 20
Eroded sand moving ‘downstream’
Similar story with the Duluth breakwater
Blocks sediment supply from north-shore bluff erosion
But sediment supply from north shore is significantly smaller
The ‘infrastructure’ problem: Starvation

## Slide 21
Sand budget:
40,000 m3/yr sand
(2001 ACOE estimate ~ 50,000 m3/yr)
Bluff erosion alone can close sand budget (little river input):
35 km of bluff x 10% sand x 40 cm/yr retreat rate x 30 m total bluff height = 40,000 m3/yr sand
The ‘infrastructure’ problem: Starvation
This is the ‘south end’ deficit

## Slide 22
Modern sand sources: What about the St. Louis River?
1861
1938
2017
Note progressive drowning of RELICT (inactive) SAND levees over 160-year timespan
Little sand was reaching Spirit Lake in 1860 (pre-dam era)
Where was it deposited?

## Slide 23
Modern bayhead delta (pre-dam sand depocenter)
St. Louis could deliver sand to lake (strandplain) during 4.5 – 1.2 kyr BP RLL fall
Onset of RLL rise at 1.2 kyr BP drowned river mouth and drove depocenter ‘upstream’
Last position (pre-dam) was Fond du Lac
St. Louis sand supply connected to lake
progressive
disconnection
progressive ‘back-stepping’ of sand depocenter

## Slide 24
Modern sand sources: What about the Nemadji River?
gage = dredged  no Nemadji sand leaves harbor
Take-home message:
All Nemadji sand trapped in harbor (and then dredged)
Significant mud transfer to lake (visual confirmation)
14,000 tons/yr ~ 6300 m3/yr
Small fraction of 35,000 – 50,000 m3/yr needed

## Slide 25
Dredging prevents Nemadji from maintaining weak connection to the lake side of the barrier
Note: Nemadji outlet would drown naturally, regardless of dredging activity, albeit at a reduced rate
Modern sand contribution from Nemadji is minimal
Modern sand sources: What about the Nemadji River?
Dredging ‘pinches off the bud’ of the Nemadji

## Slide 26
Summary / conclusions
Minnesota Point (barrier island) ~ 1000 years in age (+/-)
  14C dates (Kremmin et al.) do not refute (oldest age ~ 800 yrs BP)
Dominant sand source = south-shore bluff erosion
St. Louis & Nemadji rivers contribute minimal sand to the lake side of barrier
Breakwaters trap sand flux and starve the barrier
(partial) armoring strategies will simply shift locus of erosion towards center of barrier

## Slide 27
Final thoughts
For their size, barrier islands are the most dynamic / ephemeral landforms on Earth
Chandeleur Islands (Mississippi delta)
NASA Earth Observatory
Katrina
Drowned:
Sea level rise & sediment compaction (subsidence)
Starved:
Trapping of sand supply behind upstream dams
Battered:
Increasing frequency and magnitude of tropical cyclones
Geologic literature replete with examples of barrier systems reaching ‘tipping point’ from which there is no recovery

## Slide 28
Final thoughts
For their size, barrier islands are the most dynamic / ephemeral landforms on Earth
Drowned:
Long-term lake level rise
Starved:
Trapping of sand supply behind breakwaters
Battered:
Increasing frequency and magnitude of mid-latitude cyclones
Drawing: ACOE (2001)
X
X

## Slide 29
Thanks!
Questions?
218-726-6844
jswenso2@d.umn.edu